## Slide 1: Overall strategy
Align targets to National Policy Statement
  Phytoplankton (trophic state)
  TN, TP (trophic state)
  Ammonium (toxicity)
  E. coli (human health)
  Cyanobacteria (human health)
  Submerged plants (native – ecosystem health)
  Submerged plants (invasive – ecosystem health)
  Lake bottom DO
  Mid hypolimnetic DO
Investigate potential harmful side-effects on
  Fish
  Macroinvertebrates
  Bottom sediments

## Slide 2: Range of lake restoration actions
Bubble plume destratification*
Weed harvesting*
Wave barriers
Sediment capping
Floating wetlands*
Phosphorus inactivation*
Oxygenation
Ultrasound*
Hydrogen peroxide
Hypolimnetic siphoning
Dredging*
Surface mixers
Inflow diversion*
Inflow flushing*
Grass carp introductions*
* Currently or previously used in New Zealand

## Slide 3: Lake restoration actions
Bubble plume destratification
Weed harvesting
Wave barriers
Sediment capping
Floating wetlands
Phosphorus inactivation
Oxygenation
Ultrasound
Hydrogen peroxide
Hypolimnetic siphoning
Dredging
Surface mixers
Inflow diversion
Inflow flushing
Grass carp introductions

## Slide 4: Bubble plume destratification
Issue: Vertical transfer of heat, dissolved oxygen and nutrients greatly reduced as lake stratifies
Effects: Stratification causes
  Deoxygenation of lower water layer and bottom sediments (depending on oxygen depletion in the bottom layer)
  Increased nutrient release associated with anoxia
  May lead to dominance of buoyant, cyanobacteria, leading to blooms

## Slide 5
Bubble plume destratification Method

## Slide 6
Destratification
Increased oxygen in bottom waters
and sediments
Reduced releases of nutrients
Bubble plume destratification Expected effects

## Slide 7: Bubble plume destratification Difficulties
Timing
  Recommended to begin destratification during mixed phase (in both polymictic and monomictic lakes)
  Destratification effect: physical: immediate, ecological change: varies (e.g., phytoplankton communities)
  Long term: deep re-oxygenation of bottom sediments
Destratification can be incomplete (Sherman et al.)
Disturbance of bottom sediments from bubble plumes (when first switched on)
Increased oxygen demand of bottom sediments from increased temperature
(Re)-distribution of nutrients and phytoplankton through the water column; concentrations may be higher with destratification for some cases (Sherman et al.)

## Slide 8
Continuous (high-frequency sensors)
Temperature
  Thermistor chain(s) throughout water column at distances where it is desirable to achieve destratification
DO
  At least one sensor in the lower water layer
  Additional oxygen sensors for surface waters
Optional: Chlorophyll and/or phycocyanin fluorescence
  Surface sensor, calibrated
Bubble plume destratification Monitoring implications (split into effect-based monitoring (positive) and negative (side effects))

## Slide 9
By sampling
Nutrient profiles
  Complement routine (e.g., monthly) sampling (TN, TP, PO4-P, NOX-N, NH4-N, clarity) with increased frequency before and after (~1 month) implementation
Phytoplankton fluorescence profiles combined with chlorophyll a and cell counts
Zooplankton (as indicator of recovery)
Monitor sediment resuspension (suspended solids, turbidity in deeper waters)
Bubble plume destratification Monitoring implications

## Slide 10: Phosphorus inactivation
Issue: High phosphorus concentrations lead to eutrophication
Seasonal stratification leads to anoxia of bottom waters and phosphorus releases from bottom sediments

## Slide 11
Phosphorus inactivation Method
Add Alum (aluminium sulphate), Phoslock (lanthanum-enriched bentonite) or Aqual-P (modified zeolite)
Suspended P flocculates -> deposition in sediment
Activated sediment flocculant designed to reduce P releases

## Slide 12
Reduced reactive P – both in water column and in bottom sediment
Phosphorus inactivation Expected effects

## Slide 13: Phosphorus inactivation Difficulties
Changes in grazing pressure (use zooplankton as ecological indicator)
Phoslock:
  Settling speed (hours to days)
  Can settle on macrophytes – does not reach bottom sediment
  Potentially toxic to juvenile fish/zooplankton/macroinvertebrates
Suppression of nitrification
Acute toxicity:
  Loss of buffering with excessive Al doses can create high levels of acidity and fish kills. Shock doses likely require buffering.

## Slide 14
Phosphorus-focused monitoring: multiple timescales
  Short term – monitoring of flocculation (sediment traps + visual survey), water column measurements
  Medium term – measurements in the water column
  Long term – monitoring of P trends in sediment – bottom-sediment composition and potential releases?
Phosphorus inactivation Monitoring: effectiveness

## Slide 15
Fish
  Effects of Phoslock on juveniles
  pH effects: potential acute toxicity
Zooplankton (short scale)
  Can get trapped in flocculation clusters
  Potential to interfere with growth rates
Benthic invertebrates
  Bioaccumulation has been demonstrated in crayfish and Asian clam
  Potential effects on kakahi?
Phosphorus inactivation Monitoring: side effects

## Slide 16: Weed removals
Egeria densa
Elodea candensis
Lagarosiphon major
Ceratophyllum demersum

## Slide 17: Weed control
A long-term undertaking using harvesting

## Slide 18
Weed harvesting
Weeds Two control mechanisms

## Slide 19: Weed harvesting Difficulties
Potential to ‘flip’ the lake into different state
Instead of being sequestered, nutrients can stay in the water column
Timing of harvesting can optimise both weed and nutrient removal

## Slide 20
Weed surveys
Weed harvesting Monitoring: effectiveness

## Slide 21
Weed harvesting Monitoring implication: side effects
Nutrients in water/nutrients in weeds
  Wet vs dry weight
  TN/TP
  Before/after harvesting
Species composition
  Weed species (some can increase)
  Native plant species (can decrease)

## Slide 22
Weed harvesting Monitoring implication: side effects
Optionally fish/invertebrates

## Slide 23
Weed harvesting
Grass Carp (Ctenopharyngodon idella)
Weeds Two control mechanisms

## Slide 24: Grass carp Difficulties
Grass carp can also decimate native aquatic plants
Other effects of grass carp are not widely studied, but some indications of
  Transmission of parasites
  Changes in water quality, increased phytoplankton density
  Shifts in macroinvertebrate communities
  Reduced waterfowl by removal of macrophytes
  Altered trophic structure
Removal of grass carp

## Slide 25
Weed surveys
Adaptive management to determine optimal stocking density
Grass carp Monitoring: effectiveness

## Slide 26
Weed harvesting Monitoring: side effects
Trophic status (TN/TP)
Species composition
  Weed species
  Native plant species (LakeSPI)
  Benthic communities (change in structure)

## Slide 27
Weed harvesting Monitoring implication: side effects
Potentially additional monitoring for
  Zooplankton species composition

## Slide 28
Weed harvesting Monitoring implication: side effects
Potentially additional monitoring for
  Zooplankton species composition
  Fish communities and size classes

## Slide 29: Dredging Issue

## Slide 30
Dredging Method/effect
Mechanical nutrient/sediment removal

## Slide 31
Reduced reactive P – both in water column and in bottom sediment at longer durations
Dredging Expected effects

## Slide 32: Dredging Difficulties
Continuing maintenance
  3-year recurrence (Liu et al 2016)
Issues with dredging disposals
  PCP and PCDDs/PCDFs
  Heavy metals
Issues with remobilization
  Sediments (turbidity)
  Heavy metals
Impact on biota (can be mitigated though)
  Mussels
  Fish

## Slide 33
Monitor nutrients and total suspended solids in water column
Dredging Monitoring: effectiveness

## Slide 34
Dredging Monitoring: side effects
Heavy metal assays
Benthic biota
  Inverts
  Kakahi
  Fish

## Slide 35: Ultrasonic Issue

## Slide 36
Ultrasonic Method/effect

## Slide 37
Ultrasonic Expected effects (note – almost all in lab)

## Slide 38: Ultrasonic removal of BG algae Difficulties
Continuing maintenance
  Has to recur every 3 years (Liu et al 2016)
Issues with dredging disposals
  PCP and PCDDs/PCDFs
  Heavy metals
Issues with remobilization
  Sediments (turbidity)
  Heavy metals
Impact on biota (can be mitigated though)
  Mussels
  Fish